## Slide 1: Mapping of Majuro Atoll using a low-cost UAV
Maria Kottermair
University of Guam
Andrea Jalandoni
Griffith University
Pacific Islands GIS&RS User Conference
November 30, 2016

## Slide 3
Laura
Majuro
8.8 km2
Big picture: 1-meter DEM from Majuro to Laura
Our Goal: Map using low-cost UAV
In 10 days!
Notes: 2185 acres

## Slide 4
DJI Phantom 4
DJI Phantom 3 Pro
28’ max flight time
3+ miles-range
Better camera
23’ max flight time
~1 miles-range

## Slide 5: Survey Parameters
40-meter buffer around shoreline increased size by 57 %
(8.8 km2 => 13.8 km2)
Altitude 125 m
Photograph resolution = 2.3 cm/pix
Post-processed resolution = 5.4 cm/pix
75% Side and Front Overlap
Vertical and oblique data sets

## Slide 6: Concurrent surveys
Survey-grade GPS receivers & total station

## Slide 7: Concurrent surveys
Survey-grade GPS receivers & total station

## Slide 10: Flight path & Camera locations

## Slide 11: Challenges
HARDWARE
  Failure – RF interference??
  Overheating
SOFTWARE
  No-fly zones
  App restrictions

## Slide 12: Challenges
ENVIRONMENT
  Weather
  Glare
  Tides
  Takeoff location
LOGISTICS
  Charging battery
  Transportation
  Targets
HUMAN ERROR
  Wrong settings

## Slide 13: Preliminary Results/ Post-Processing (SfM) using Agisoft PhotoScan

## Slide 14
Results
44 missions
Over 36,000 pictures
Preliminary results promising
Conclusions
Combining vertical and oblique requires more flights and photogrammetry processing but better results
Consumer-level UAV (<2k USD) can be used for high-resolution mapping
Promising tool for Pacific Islands

## Slide 15: Next steps…
Continuous Orthomosaic
1-meter resolution DEM

## Slide 16: Acknowledgements
USGS Pacific Islands Climate Science Center
USGS Coastal National Elevation Dataset
NOAA National Geodetic Survey
University of Hawaii
University of Guam
RMI Lands & Survey
Directorate of Civil Aviation
MI Conservation Society
SeaGrant

## Slide 17: Vinaka!