## Slide 1: - Reef to Coast - Airborne mapping of developments in the coastal region
Presented by
Veroniva Macovei and Dr. Holger Eichstaedt

## Slide 2: Objectives
Efficient and fast mapping for:
  Engineering, planning and preventive maintenance
  Identification of climate change effects
  accessing Environmental impact and monitoring pollution
  Establishment of baselines
Available also under conditions like difficult accessibility, large areas required, complicated weather conditions

## Slide 3: Technical solution
Multisensory airborne approach combining required sensors in one flight:
  Topographic and bathymetric airborne Lidar systems with full waveform data collection
  Hyperspectral sensors in different bands (reflective VNIR and SWIR, thermal LWIR)
  Multiple digital camera systems
  Airborne Radar in different bands
Guided through GPS and all data orientated by GNSS and Inertial systems

## Slide 4
Between satellite scale
  better spatial and spectral resolution for direct engineering and mitigation work
  but higher costs than satellites
and UAV scale
  more and calibrated sensors
  working under more complex weather conditions
  efficient also above 3 sqkm
Positioning of the technical solution of airborne operations

## Slide 5: Technical solution

## Slide 6: Technical solution

## Slide 7: Technical solution
Multisensory airborne approach combining required sensors in one flight:
  Topographic and bathymetric airborne Lidar systems with full waveform data collection
  Hyperspectral sensors in different bands (reflective VNIR and SWIR, thermal LWIR)
  Multiple digital camera systems
  Airborne Radar in different bands
Guided through GPS and all data orientated by GNSS and Inertial systems

## Slide 8: Technical solution
Data processing:
  With or without ground control point
  Accuracies for Lidar data within 10cm for topography and 20cm for bathymetry
  Image and hyperspectral data with between 0.5 and 1.5 pixel accuracy (0.03 to 3m depending on sensor and
  Airborne Radar in different bands 0.5 to 3m accuracy
Data fusion to object based approaches, 3D objects and thematic maps according to client request

## Slide 9: Results and Examples - 1
Combined bathymetric/topographic mapping of the aquatic interface using a dual frequency Lidar solution for planning, infrastructure, estimation of climate change effects and flood modelling
  Dual Lidar green in 634nm and IR in 1550nm
  Flying height: 600m
  Swath width (overlap 30%): 350m
  Penetration: 1 to 1.5 Secchi depth
  Point densities: 1 per sqm for bathymetry, 8 per sqm for topography
Productivity: approx. 15 to 30 sqkm/flight hour

## Slide 10
Sending two Laser beams out
  green for water depth
  infrared for topographic mapping

## Slide 11: Accuracy considerations and ground

## Slide 15: Results and Examples - 2
Integration of Hyperspectral VNIR into the solution for mapping of Reef conditions, vegetation, chlorophyll, turbidity and water pollution
  Flying height: still 600m
  Same flight as dual Lidar solution
  Spectral resolution: 160 bands in 400 to 1000nm
  Spatial resolution: 0.3 to 0.5m

## Slide 16: Marine System - Coral Reef Example
A true color image of îlot Maître – New Caledonia (based on VNIR Hyperspectral data)

## Slide 17: Spectral difference

## Slide 18: Decision Tree final classification result

## Slide 19: Further analysis
Different coral group can be extracted for further analysis
Ground truth will be needed for coral group identification

## Slide 20: Turbidity Example
Less turbid
More turbid

## Slide 21: Chlorophyll-a
Lower concentration
Higher concentration

## Slide 22: Total Phosphorus (TP) - îlot Maître (NC)
Lower concentration
Higher concentration

## Slide 23: Incident Mapping - Pellets Pollution Example
pellets (also other plastic components)

## Slide 24
With laboratory results, a spectral library is built and pellets detection is performed
Detection results have been proven to show pellets distribution

## Slide 25: Results and Examples - 3
Integration of Hyperspectral VNIR and SWIR into the solution for mapping of land vegetation, soils, detailed land use, forestry and agricultural parameters, geotechnical facts, pollution on land
  Flying height: still 600m
  Same flight as dual Lidar solution
  Spectral resolution: 416 bands in 400 to 2500nm
  Spatial resolution: 1m

## Slide 26
Forestry Map

## Slide 27: Forestry Map

## Slide 28: Heavy metal pollution

## Slide 29
Mineral and Mining maps

## Slide 30: Results and Examples - 4
Integration of thermal broadband or hyperspectral for polluter analysis
  Flying height: still 600m (for broadband), 1000+m for thermal hyperspectral
  Same flight as dual Lidar solution (for thermal hyperspectral additional flight)
  Spectral resolution: 130 bands in 7800 to 11800nm
  Thermal resolution: better 0.018K
  Spatial resolution: 1m

## Slide 31: Industrial pollution
Changes in water temperature identified

## Slide 32: Domestic pollutions and freshwater seapages

## Slide 33: Analysis of pollution effects along the coast line
The ship berthed at the wharf prevents the warmer water drifting northwards
Warmer water collects against the shoreline

## Slide 34
Thanks for your attention
and please feel free to ask any question
Holger@helipro.com.fj